## Slide 1: Mass Spectrometry-based Proteomics
Phil Gafken
Director, Fred Hutch Proteomics Resource
05/09/22 to 05/13/22

## Slide 2
Course Outline
What is Proteomics?
Mass Spectrometers
  Ionization
  Analyzers
  Dissociation
The Mass Spectrum
LC-MS & FAIMS
Tuesday Teams
-LC-MS/MS
-Orbitrap Eclipse
Protein Identification
Protein Database Searching
Peptide Validation
Linking Peptide IDs to Proteins
Wednesday Teams
-Modification Analysis
-Serum Proteomics
-Facility Tour
Thursday Teams
Sample Preparation
Protein Quantification
Monday Teams
Friday Teams
-Emerging Topics in Proteomics (kinda)
  -Targeted Proteomics
  - MHC Peptides
  - Laser Capture Microdissection
-Proteome Discoverer 2.5 Demo
-Course Survey

## Slide 3: Sample Preparation
Proteins and peptides must be in a form that
is compatible with LC-MS.
Good separation and purification techniques are
critical for good LC-MS.
Good LC-MS = Good results!
Only covering sample preparation for bottom-up methods

## Slide 4
General Sample Preparation Scheme
Protein Isolation
Protein Fractionation
Digestion
Peptide Fractionation
(Bottom-up Proteomics)
Cell culture
Tissues
Serum/plasma
1D/2D gels
Chromatographic
Trypsin
Lys-C
Tryp/LysC
Glu-C
Chymotrypsin
SCX
Basic-RP
Desalting
(optional)
(optional)
One or the other is performed

## Slide 5
Protein Isolation: Lysis/Solubilization
(Bottom-up Proteomics)
Denaturing Buffers
SDS
Urea
RapiGest
Typical Use
Thorough protein denaturation
Global proteome and PTM analysis
Non-Denaturing Buffers
Triton
NP40
RIPA
Maintains protein complexes
Affinity proteomics
Typical Use
Physical Disruption
Sonication
Cryo-pulverization
Beads
Pressure
Protease inhibitors typically added (phosphatase inhibitors usually added for phosphoPTM experiments)
Maintaining high sample concentration is important (> 1 µg/µL for global expts)

## Slide 6
Protein Fractionation by 1D SDS-PAGE
SDS-PAGE = Sodium Dodecyl Sulfate Polyacrylamide Gel Electrophoresis
Protein Mixture
Denature with SDS
(negatively charged detergent)
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
t0
+
-
+
+
+
t1
t2
t3
-
-
-
PAGE
PAGE
Stain gel to visualize
protein bands

## Slide 7
Protein Fractionation by 2D SDS-PAGE
Protein Mixture
Add SDS
Join to polyacrylamide gel
Isoelectric focusing
-
+
+
-
Orthogonal separation allows for better resolution as compared to 1D gels
pH gradient
(i.e. pH 4 to pH 9)

## Slide 8
Protein Fractionation by Gel
You might want to know…
In Gel:
  Acrylamide % isn’t a problem; TAU gels work also
  Virtually any type of gel system works
  Coomassie- or silver-stained bands are okay
  Unstained gels are possible (rainbow markers to define regions)
  Multiple proteins in a band aren’t a problem
  Gels are fantastic for removing protein lysis/solubilization reagents
  Gels can separate contaminating proteins (H/L chain)
  Denaturing condition of gel aids digestion
  Maintain information about protein’s MW will gel MW markers

## Slide 9
I
time
t0
t1
t2
t3
t4
t5
Stationary
Phase
Liquid
Phase
Protein Fractionation in Solution

## Slide 10
Types of Liquid Chromatography
Type
Mode of Separation
Cation or anion exchange
+ or - Charge
Reverse phase
Hydrophobicity
Size exclusion
Size
Affinity
Specific functional groups

## Slide 11
Protein Fractionation in Solution
You might want to know…
In Solution:
  More sensitive than gels? (peptide recovery less of an issue?)
  Contaminants are more of a problem, especially detergents
  pH must match digestion conditions
  Volume must be controlled (< 500 uL); protein ppt (TCA, acetone
  might be useful)
  Multiple proteins present aren’t a problem
  Protein fractionation is frequently skipped, and complex mixtures can be simplified by peptide fractionation methods

## Slide 12
Protease Digestion
HPLC fraction
or
IP elution
Solution digestion
1. Adjust pH
2. Reduce and Alkylate
3. Digestion
Gel slice digestion
Cut band from gel
1. Wash
2. Reduction & alkylation
3. In-gel digestion
4. Elute peptides
(1D or 2D)
1.
5. Reduce elution volume
1. Wash
Cut band from gel
(1D gel)
2.
2. Reduction & alkylation
3. In-gel digestion
4. Elute peptides
5. Reduce elution volume
desalt
desalt
desalt

## Slide 13
Protease Digestion
1. Reduction: Dithiothreitol (DTT), TCEP, β-mercaptoethanol
R1
S
R2
S
R1
SH
R2
SH
Both steps usually performed under denaturing conditions
56℃
Don’t exceed 56℃ in presence of urea (carbamylation)
+
2. Alkylation: Iodoacetamide, chloroacetamide, MMTS
CH2-S-H
+
I-CH2-C-NH2
= O
CH2-S
-CH2-C-NH2
= O
+
HI
RT, dark
Don’t use IAA for ubiquitin proteomics (IAA lysine adducts mimic diGly Ub tag)

## Slide 14
Protease Digestion
You might want to know…
Proteases:
  Trypsin is most common protease used
    Cleaves after K &R (reduced activity for KP and RP)
    Cheap and readily available
    Generally produces peptides 700-3000 Da; ideal for MS
    Very active in both gel and solution (urea < 2 M)
    Autodigestion needs to be controlled; keep cool until ready to activate with protein
  pH, amounts of salts and detergents must be controlled
  Other proteases work well in solution but are difficult to use in -gel(?!)
    Lys-C active at high urea concentrations
    Lys-C at high [urea], followed by trypsin at lower [urea]
    Other proteases used for peptide mapping
  Knowing starting amount of protein very helpful for optimizing digestion

## Slide 15
Peptide Fractionation
Most common methods:
Strong cation exchange chromatography
Basic reverse phase chromatography
Isoelectric focusing
These methods provide a first dimension of separation
LC-MS provides a second degree of fractionation
Divide the complex mixture into less complex fractions that are more amenable to LC-MS
Goal:

## Slide 16
Peptide Fractionation
(complex mixtures)
Time (min)
Amplitude (mAU)
Strong-Cation Exchange Chromatography
Proteins
Peptides
SCX
- Fractions are pooled, desalted and run by MS
- Separation is based on solution charge of peptide (+1, +2, +3, +4)
- Limited fractionation ability

## Slide 17
Peptide Fractionation
(complex mixtures)
Basic Reverse Phase Chromatography
Proteins
Peptides
bRP
- Separation based on hydrophobic properties of peptides
- Fractions are pooled and taken to dryness (usually 24 pools)
- Generally, a more even distribution of peptides over chromatogram
- Standard reverse phase separation, but performed at pH 8
- Volatile elution buffer that can be removed by vacuum centrifugation
Pooling scheme: Pool 1 = F1, F25, F49, F73; Pool 2 = F2, F26, F50, F74; etc.

## Slide 18
Peptide Desalting
ZipTips (Millipore)
C18 (5-10 µg)
µC18 (2-5 µg)
SCX
OASIS Cartridges (Waters)
Multiple sorbent types
Up to 100 µg
Numerous companies sell desalting devices
P200 tip

## Slide 19
Carol Farr and Julie Saugstad
R.S. Dow Neurobiology Lab
Portland, OR
The Need for Good Sample Prep
(an example)
Identification of proteins that interact with
metabotropic glutamate receptors 1 & 5

## Slide 20
1. Protein complex in solution
2. Antibody capture of complex
3. Elute purified complex
LC-ESI MS/MS
Proteolytic digestion
“Shotgun approach”
Immunoprecipitation
experiment
(Solution vs. Gel )
The Need for Good Sample Prep

## Slide 21
Total Ion Chromatogram
Solution digest
of protein
complex
m/z
m/z
m/z
m/z
(Solution vs. Gel )
The Need for Good Sample Prep

## Slide 22
1. Protein complex in solution
2. Antibody capture of complex
3. Elute purified complex
LC-ESI MS/MS
+
-
Cut Regions
In-gel
Proteolytic
digestion
SDS-PAGE
(Solution vs. Gel )
The Need for Good Sample Prep

## Slide 23
STDs
kDa
198
114
96
53
36
28.5
18.5
J
I
H
G
F
E
D
C
B
A
Lane
Slices
antibody
Lane 1 = mGluR1
Lane 2 = mGluR5
Lane 3 = CB
1
2
3
1
2
3
Gel purification
of IP samples
Sample processing
performed on
unstained gels
J. Neurochem. 91:438 (2004)
(Solution vs. Gel )
The Need for Good Sample Prep

## Slide 24
(Solution vs. Gel )
The Need for Good Sample Prep
Total Ion Chromatogram
Gel slice digestion

## Slide 25
(Solution vs. Gel )
The Need for Good Sample Prep

## Slide 26
What is Not Compatible with LC-MS
Reagent | Why it is not compatible | How to deal with it
Detergents | - Dominates mass spectra; mass spec. spends it time only on detergent signals - Suppresses signal of peptides - Trashes instrument | - Protein Precipitation - Run into gel - Avoid using them - MS-friendly detergent - Removal tips (New!)
Salts | - Non-volatile; dirties instrument; more frequent cleaning of instrument | - Desalting!
Perfluoronated acids (e.g. TFA, HFBA, HFIP) | - Dramatically reduces sensitivity of instrument; has long “memory effect”! | - Speed vac to remove (volatile) - Use formic or acetic acid
Non-volatile organic solvents (e.g. DMSO, DMF) | - Negatively alters HPLC | - Dilute if possible - Avoid using them

## Slide 27
Protein Quantification
Label-free and isotopic labeling approaches

## Slide 28
Representation of Shotgun Data
(MS with MS/MS data)
Intensity
Time (scan#)
1
2
3
4
MS
MS
MS
MS
MS/MS
MS/MS
MS/MS
MS/MS

## Slide 29
Spectral Counting
 | ORBITRAP_50fmol_UPS49_03.pep.xml (040207/LN040507_50fmol_UPS49_03 (UniprotHum_RA_20070222)) | ORBITRAP_5fmol_UPS49_02.pep.xml (040207/LN040207_5fmol_UPS49_02 (UniprotHum_RA_20070222))
Protein | Total | Total
IPI00022389 | 6 | 1
IPI00022434 | 30 | 5
IPI00022463 | 36 | 9
IPI00026314 | 8 | 4
IPI00027487 | 14 | 5
IPI00028064 | 7 | 1
IPI00032291 | 6 | 2
IPI00218414 | 13 | 6
IPI00219684 | 10 | 2
IPI00219757 | 12 | 2
IPI00288914 | 3 | 1
IPI00413587 | 12 | 2
IPI00465315 | 6 | 3
IPI00479848 | 9 | 2
P02788¦TRFL_HUMAN | 35 | 11
P04040¦CATA_HUMAN | 24 | 14
P35527¦K1C9_HUMAN | 16 | 10
PIR1:AQHUP | 11 | 5
PIR1:CSHUA | 7 | 1
PIR1:HAHU | 6 | 1
PIR1:HBHU | 9 | 7
PIR1:KRHUEA | 13 | 7
UPSP:ANT3_HUMAN | 14 | 7
gi¦51703341 | 2 | 
GP:AL031058_1 | 2 | 
IPI00000073 | 1 | 
IPI00001671 | 1 | 
IPI00009867 | 7 | 
IPI00012009 | 1 | 
IPI00017730 | 1 | 
IPI00019524 | 1 | 
IPI00022429 | 1 | 
IPI00025753 | 1 | 
IPI00027547 | 1 | 
IPI00032957 | 2 | 
IPI00216298 | 3 | 
IPI00218733 | 2 | 
IPI00219018 | 1 | 
IPI00293665 | 1 | 
IPI00303105 | 5 | 
Total spectra matched to each protein in each run is compared
# of MS/MS identifications can be related to abundance
No labeling is required

## Slide 30
Qualities of Spectral Counting
Low cost (does not require costly reagents)
Minimal changes to standard sample prep
Spectral counts come for “free” with protein identification results
Summary details:
Pros:
Cons:
Low quantitative precision
Low/no peptide counts can be unreliable (small proteins, low abundance, low observations)
High sample handling variability
No multiplexing; replicates help with confidence (increased analytical burden)
Analytical conditions for each sample must be identical
Only useful for comparing a protein across samples
Relative quantitative method
Typical Use:
For general quantitative view
Immunoprecipitations
After thought (after seeing results)

## Slide 31
Total Ion Chromatogram
(measure total signal from all ions over time)
Survey Scan
Reconstructed Ion Chromatogram
(measure single ion over time)
Label Free Quantification
*
*
Run#1
Run#2
Run#1
Run#2

## Slide 32
Qualities of Label-Free Quant.
Low cost (does not require costly reagents)
Minimal changes to standard sample prep
Software for quantification is available (MaxQuant, Proteome Discoverer)
Summary details:
Pros:
Cons:
Intermediate quantitative precision
High sample handling variability
No multiplexing; replicates help with confidence (increased analytical burden)
Analytical conditions for each sample must be identical
Sum peptides for a protein; shared peptides are usually omitted from quantification
Relative quantitative method; intensity or peak area can be used
Typical Use:
Low complexity samples; low sample amounts
Immunoprecipitations
After thought (after seeing results)

## Slide 33
SILAC
(Stable Isotope Labeling with Amino acids in Culture)
A
B
Cells grown in culture and fed
essential, isotopically labeled
amino acid (i.e. 13C6-arginine)
light
heavy
Pool Samples
Harvest Proteins
Trypsin Digestion
Resulting in Peptide Mixture
Mass Spectrometry
Labeling kits sold
by many vendors
OH
=
O
N
H
H2N
=
NH
NH2
Arg+0(Light)
OH
=
O
N
H
H2N
=
NH
NH2
Arg+6(Heavy)
13C
m/z
Intensity
A
B
6 Da
MS1

## Slide 34
Very high quantitation precision
Combining samples prior to protein extraction minimizes downstream handling errors
Applicable to protein modifications
Qualities of SILAC
S. Ong, et al: Mol Cell Proteomics 1 (2002) 376-386
S. Ong, I. Kratchmarova, and M. Mann: J. Proteome Res 2 (2003) 173-181
S. Ong, L.J. Foster, and M. Mann: Methods 29 (2003) 124-130
* C.C Wu, et al: Anal Chem 76 (2004) 4951-4959
Summary details:
Isotopically labeled, essential amino acids used (13C6, 15N4-Arginine (+10) and 13C6, 15N2-Lysine (+8) )
Potential to label all proteins
Multiple peptides per protein for quantification
Quantification measurements are relative
Shared peptides usually omitted from quantification
Pros:
Cannot be used for primary tissue and fluids (caveat: isotopically labeled mouse)*
Expensive
System must be SILAC compatible
Increases the complexity of the mass spectrum due to isotopic pairs
Low degree of multiplexing
Cons:

## Slide 35
SILAC: Label Swapping
Cell Line A
Cell Line B
Experiment 1
Mix 1:1
Light
Heavy
Cell Line B
Cell Line A
Experiment 2
Mix 1:1
Light
Heavy
-3 -2 -1
1 2 3
1 2 3
-3 -2 -1
Exp 1: Log2 (Cell line B/Cell line A), H/L
Exp 2: Log2 (Cell line B/Cell line A) L/H
Contaminant
proteins
Up-regulated
proteins
Down-regulated
proteins
Unchanged
proteins

## Slide 36
Example of SILAC Experiment
L
H
(Identification of long-lived proteins)
- H/L > 0.1 indicates long-lived protein
Slide courtesy of Nate Thayer and Dan Gottschling
PNAS 111:140 (2014)
Pulse-chase experiment

## Slide 37
Example of SILAC Experiment
(Identification of long-lived proteins)
Dot size represents relative amount of peptides in that slice
Red line is expected MW of protein
- Full-length and fragmented proteins identified
- Cell wall proteins (BGL2) are known to remain with the mother throughout her lifespan
Slide courtesy of Nate Thayer and Dan Gottschling
PNAS 111:140 (2014)

## Slide 38
Example of SILAC Experiment
(Identification of long-lived proteins)
YML052W_SUR7 (Plasma membrane protein)
LASTYSIDNSR
H/L = 0.525

## Slide 39
iTRAQ
Isobaric Tags for Relative and Absolute Quantification
Reporter Group
Peptide Reactive Group
Balance Group
Fragmentation Site
13C
15N
18O
114 +
31
115 +
30
116 +
29
117 +
28
Fragmentation
H+
114
115
116
117
All reagents have the same mass
H+
H+
H+
P.L. Ross, et al: Mol. Cell. Prot. 3.12 (2004) 1154-1169

## Slide 40
Multiplex Processing
Sample 2
Reduce, Alkylate,
and Digest
Digest 2
Tag 2 Peptides
Tag 115
Sample 3
Reduce, Alkylate,
and Digest
Digest 3
Tag 3 Peptides
Tag 116
Sample 4
Reduce, Alkylate,
and Digest
Digest 4
Tag 4 Peptides
Tag 117
Sample 1
Reduce, Alkylate,
and Digest
Digest 1
Tag 1 Peptides
Tag 114
Combine Peptide Mixtures
Fractionate, MS Analysis
4-plex experimental setup
Condition 1
Condition 2
Condition 3
Condition 4
114
115
116
117
iTRAQ

## Slide 41
The Mass Spectra
Since the iTRAQ labeling reagents are isobaric, identical peptides from different
samples have the same mass (in MS1).
m/z
Intensity
0
2000
Abundance ratios are:
1:4:4:2
Intensity
m/z
110
120
114
115
116
117
M2 spectra
B- and y-ions are present
allowing for identification
of peptide
Reporter fragment ions are present in MS2 that allow quantification of the peptide in
each sample
Fragment ions for identifying the peptide are also present
m/z
Intensity
0
2000
M1 spectra
Selection of precursor ion for MS2
iTRAQ

## Slide 42
iTRAQ
Co-isolation problem
Ion selected for MS2 may not be pure
Ions with very close m/z will also be selected
“Contaminating” ions the MS2 spectra will reduce the accuracy of the quantification, typically compressing the quantitation ratios
Synchronous precursor scanning (MS3) can eliminate ratio distortion, but at reduced data collection rates (increased quant. accuracy, but reduced protein ids)
m/z
Intensity
0
2000
M1 spectrum
Selection of precursor ion for MS2
MS2 Spectrum
Quantification
Nature Methods 8, 937 (2011)

## Slide 43
Qualities of iTRAQ
Summary details:
Pros:
Cons:
Potential to label all proteins
Multiple peptides per protein for quantification
Quantification is relative
Could be used for time course experiments
Multiplexing up to 8 samples (very cool), 18-plex for TMT (Thermo) is available
Reasonably high quantitation precision
Can be used for clinical samples (biopsies, fluids)
Applicable to protein modifications
Extensive sample labeling biochemistry (not so much a “con” as a warning)
Samples combined after protease digestion
Expensive
Co-isolation of precursor ions can reduce quantitative accuracy
P.L. Ross, et al: Mol. Cell. Prot. 3.12 (2004) 1154-1169

## Slide 44
Example of iTRAQ Experiment
(N. gonorrhoeae therapeutic targets)
- Neisseria gonorrhoeae is second most commonly reported infection in the US
- Infections cause all sorts of problems (genital infections, blood infections, PID, ectopic pregnancy, infertility)
- Resistance to antibiotic treatment is growing; WHO estimates N. gonorrhoeae could be resistant to current drugs by 2015
- Cell envelop and membrane vesicles play a role in colonization and infection of human tissues and cell lines
- Thorough proteomic analysis of the cell envelop and membrane vesicles was performed to identify potential therapeutic targets
- Estimated 62 million cases occur each year (worldwide)
Aleksandra Sikora and Ryszard Zielke, Oregon State University

## Slide 45
765
568
308
213
Final
316 CE & 57 MV
Example of iTRAQ Experiment
(N. gonorrhoeae therapeutic targets)
Mol Cell Proteomics 13: 1299 (2014)

## Slide 46
L
115/114
116/114
117/114
1.15
1.32
1.81
Example of iTRAQ Experiment
(N. gonorrhoeae therapeutic targets)

## Slide 47
Example of iTRAQ Experiment
(SPROX-Stability of Proteins from Rates of Oxidation)
- Measures folding free energies and Kd values of protein ligand complexes on a proteomics scale
- Used to identify proteins that bind tested ligands
- Identification of drug targets
- Change in the transition midpoint for Met-peptides in (-) Ligand and (+) Ligand samples allows for free energy calculations
- H2O2 used to induce oxidation on Met as a function of denaturant concentration
Nat Protoc. 8:146 (2013)

## Slide 48
TMTpro-126
*
TMTpro-127N
*
TMTpro-127C
TMT-Pro 18plex
Reconfigured figure from Li et. al. J. Proteome Res 20, 2964-2972 (2021)
(Design)

## Slide 49
TMTpro-126
*
TMTpro-127N
*
TMTpro-127C
TMT-Pro 18plex
(Chemistry)
126.127726
Mass of Reporter Ion
13C = 13.003355
12C = 12.000000
-
1.003355
15N = 15.000108
14N = 14.003074
-
0.997034
+ 0.997034
127.124760
+ 1.003355
126.127726
127.131081
Δm = 0.006321
Reconfigured figure from Li et. al. Nature Methods 17, 399-404 (2020)

## Slide 50
TMT-Pro 18plex
(The Mass Spectrum)
MS2
MS2

## Slide 51
Absolute Quantification of Proteins by MS
AQUA
Protein
lysate
1. Trypsin digestion
2. Introduce known amount
of reference (heavy) peptide
3. LC MS/MS
4. Extracted ion chromatogram
time
18.5
18.5
Heavy- reference peptide
Light- analyte peptide
5. Quantify ratio
6. Determine protein amount
…TLSDYNIQK…
H2N-TLSDYNIQK-COOH
LC MS/MS
time
Select protein of
interest
Select tryptic
peptide for
quantification
Synthesize reference
peptide with heavy
isotopes (13C, 15N)
Characterize fragmentation
spectrum for identification
Use extracted ion chromatogram
to test quant. conditions
18.5

## Slide 52
Qualities of Absolute Quantification
Summary details:
Pros:
Cons:
Setting up can be time consuming and challenging
Synthetic peptide standards are expensive
Isotopically labeled amino acids are commercially available, synthesis of reference
peptide is almost trivial
Arginine 13C6,15N4 and lysine 13C6,15N2 increase peptide mass by 10 Daltons and 8 Dalton, respectively, as compared to light peptide
Choose a tryptic peptide which resolves well by HPLC. Avoid very hydrophobic
or very hydrophilic peptides.
Choose peptide that ionizes well
Light and heavy peptides co-elute
Method can be applied to quantifying protein modifications
(For phosporylation, see S.A. Gerber, et al: PNAS 100 (2003) 6940-6945)
Absolute quantification (not relative!) can be achieved; high precision & accuracy
Multiplexing can be performed (multiple synthetic peptides)
Method can be applied to clinical samples (serum, urine)

## Slide 53
Quantification Summary
 | Spectral Counts | Label-free Quant. | iTRAQ/TMT | SILAC | AQUA
Cost | ø | ø | $ | $$ | $$$
Multiplexing | None | None | 8/18 samples | 2-3 samples | 50-100 proteins
Sample Prep. | Low | Low | High | Medium | Very High
Precision | Low | Low | Good | Very Good | Excellent
When is “better” the enemy of “good enough”?